04 CONNECTIVITY

USE CASE INDUSTRY 4.0
Industry 4.0 (Smart Manufacturing/ Factories of the Future)
- Use of IoT to manufacturing value-chains
- Combines production methods with state-of-the-art information and communication technology towards intelligent and flexible production
The internet of connected things and services
- Smart Mobility: Thanks to intelligent traffic control, traffic jams become a thing of the past.
- Smart Grids: Networking and management of electricity producers, storage facilities,
- consumers, and grid equipment.
- Smart Homes: Improved living conditions, quality of life, and security. More efficient
- energy use due to networked devices and installations as well as automated
- processes.
- Smart Healthcare: Monitoring systems for people with chronic conditions, healthoriented exercise programs, and intelligent emergency call systems.
- Smart Factories: intelligent components and machines form networks and autonomously control production processes.
Industry 4.0 is either a subset of the “Internet of things and services” or described the overall idea of interconnecting the whole value chain

5-Layer automation pyramid

Input/ Output (I/O)
Programmable Logic Controller (PLC)
Supervisory Control and Data Acquisition (SCADA)
Manufacturing Execution System (MES)
Enterprise Resource Planning (ERP)

SCADA – Supervisory Control and Data Acquisition
- An industrial network to connect PLC’s and HMI’s with each other.
- SCADA systems are the backbone of modern industry.
- RTU = Remote Terminal Unit.
- HMI = Human Machine Interface.
MES – Manufacturing Execution System
Centralized monitoring and control instance to optimize the production
ERP – Enterprise Resource Planning
- Integration into further processes such as invoicing, order management, demand estimation, … for further optimization.
- Often not yet established in smaller/medium sized factories.

Cyber-Physical System(CPS) based automation
The idea is to have autonomous CPS‘s that communicate with each other to enable a flexible manufacturing process.

From the 5-Layer architecture to autonomous CPS

- The functionalities of the typical automation pyramid might move, step by step,
- towards CPS-based automation.

INTEROPERABILITY STACK
Different levels of interoperability

Typical network and distribution abstraction
- Network: the physical connections and protocols
- Middleware: an interoperability layer between the actual application and the network
- Application: the actual business logic (and user interface).

IIRA - Industrial Internet Reference Architecture
- Business viewpoint: attends to the concerns of the identification of stakeholders and their business vision, values and objectives in establishing an IIS in its business and regulatory context. These concerns are business--oriented and are of particular interest to business decision-makers, product managers and system engineers.
- Usage viewpoint: addresses the concerns of expected system usage. It is typically represented as sequences of activities involving human or logical users that deliver its intended functionality in ultimately achieving its fundamental system capabilities.
- Functional viewpoint: focuses on the functional components in an IIS, their interrelation and structure, the interfaces and interactions between them, and the relation and interactions of the system with external elements in the environment, to support the usages and activities of the overall system.
- Implementation viewpoint: deals with the technologies needed to implement functional components, their communication schemes and their lifecycle procedures.
These components are coordinated by activities (Usage viewpoint) and supportive of the system capabilities (business viewpoint).
IIRA – Functional domains (For a cyber-physical system)
- The functional domain identifies needed components and interfaces.
- Is the specification of a CPS
- Control domain: Functions performed by the industrial assets or control systems executing closed-loop control that may involve sensing, control and actuation.
- Operations domain: Functions for assets and control systems management and maintenance to ensure their continuing operations. These functions may include remote health monitoring, configuration and update, diagnosis and preventive maintenance.
- Information domain: Functions for collecting, transforming and analyzing data to acquire high-level intelligence of the entire system.
- Application domain: Functions for applying use-case-specific logic, rules and models based on the information obtained from the information domain to achieve systemwide intelligent and optimal operations.
- Business domain: Functions for integrating information across business systems and applications to achieve business objectives, such as work planning, customer relationship management (CRM), enterprise resource planning (ERP), manufacturing execution system (MES).

Relationship between IIC and the platform industry 4.0
While the IIC is covering most IIoT domains – energy, healthcare, manufacturing, public domain, transportation, industry 4.0 initially focused on manufacturing
RAMI - Reference architecture model industry 4.0
- RAMI is NOT a technical architecture.
- It is an abstract framework in order to encourage clear communication.
- It has high international visibility and puts three different dimentions into relation.
- Layers:
- Business(ERP): value chains, service orchestration
- Functional: integration, runtime environment, rules
- Information: persistence, data models
- Communication
- Integration: API’s for sensing and actuation
- Asset: hardware, humans
Hierarchy Levels
Based on international electrotechnical commission(IEC) 62264: Enterprise-control system integration
- Models and terminology
- Object model attributes
- Activity models of manufacturing operations management
Business to manufacturing transactions
Life cycle
- Life-cycle management for systems and products used in industrial-process measurement, control and automation
- Added object oriented paradigm (Digital twin)
- Important is the differentiation between the virtual/abstract model of products, factories and processes (digital twin) and the concrete instantiation of produced goods and controlled devices.
- Costs can be reduced by simulating and optimizing planned production processes first.

IIRA VS RAMI

The IIRA and RAMI can nicely be mapped to each other

Industry 4.0 component(CPS) – Asset administration shell (AAS)

The combination of asset and AAS is called Industry 4.0 Component
- This depicts an autonomous CPS.
- One or multiple assets are virtually represented, controlled and monitored by software (administration shell).
- The shell holds static and dynamic information about the asset(s) and offers various components to interact with the asset(s).
Missing in this figure
- the administration shell offers connectivity to other I4.0 components
- the administration shell is connected to the asset(s)

CONNECTIVITY
- Layer 1(physical) + 2(data link)
- Connectivity and interoperability
- Enable to share data between nodes within an industrial IoT system
- Provides the ability to exchange data amongst participants within a functional domain, across functional domains within a system and across systems
- Connectivity demands interoperable communications between endpoints
Industrial real-time requirements
- Within industrial domains, however, the requirements are different to typical ICT (consumer) domains.
- Hard real-time response times, very low latency, … depending on the use case.
- With usual Carrier-sense multiple access with collision detection (CSMA/CD), as used in Ethernet, or Carrier-sense multiple access with collision avoidance (CSMA/CA), as used in Wi-Fi, these requirements can’t be met
5-Layer automation pyramid - Connectivity between PLS’s over SCADA, PLS’s and the assets
- Connectivity is part of the IIRA control domain - the control domain is devided into further functional blocks. The communication block is responsible for the communication with external entities.
- RAMI – Connectivity between assets and the higher levels

WIRELESS TECHNOLOGY
- Significant annual growth.
- Often used to collect non-critical monitoring data.
- Due to the shift towards (mobile) autonmous CPS‘s, the demand for industrial
- wireless technologies will also rise.
Analog modulation
- Amplitude Modulation (AM)
- Frequency Modulation (FM)
Digital modulation
- Phase-shift keying (PSK)
- Frequency-shift keying (FSK)
- Amplitude-shift keying (ASK)
Sharing the same frequency by
- Time-division multiple access (TDMA): different time slots (hold your phone to a speaker
- Carrier-sense multiple access (CSMA): listen to the medium / use handshakes.
Others:
- Space division multiple access (SDMA): physical areas.
- Power division multiple access (PDMA): variable transmission power.
Wireless technology compared
- Differentiation of technologies based on their range.
- Important difference: licensed vs. unlicensed band
Industrial VS. Consumer IoT connectivity

Industrial IoT gateway
Gateways in order to:
- enable various industrial devices to communicate over long distances
- harmonize different connectivity technologies
- preprocess data
- I/O: sensors, fieldbus interfaces, industrial ethernet
- Local wireless connectivity: BLE, Wi-Fi
- Form factor: IO67, DIN rail
- Power: potentially optimized for low energy consumption
- Wide area connectivity: LoRa, 2G, 3G, 4G
- Identity & mobility: eSIM, roaming
- Communication: OPC UA, REST, MQTT
- Programmability: device management, updates, local analytics & actuation
- Bandwidth reduction: compression, aggregation

FIELDBUS TECHNOLOGY
Fieldbus is an industrial network system for real-time distributed control. It is a way to connect instruments in a manufacturing plant.
DIRECT CONNECTIONS VS. BUS
- Direct: Simple design, expensive, many cables, no need for addressing
- Bus: Reduction of costs and cables, easier to install, easier to extend, need for addressing
Sharing a bus (using time)
TDMA (Time Division Multiple Access)
Time-slot based, Cyclically repetitive frame structure循环重复帧结构, known from 2G cellular Systems
CSMA (Carrier Sense Multiple Access)
Statistical multiplexing, Collision Detection (CD), known from Ethernet, Collision Avoidance (CA), known from Wi-Fi
Bus system
- Use Case: Transportation, Buildings, Automation
- Requirements: Real-time latency, Bandwidth, Cable length, OSI layers
Example
Bitbus, profibus, controller area network (can) bus, AS-I actuator sensor interface

INDUSTRIAL ETHERNET TECHNOLOGIES
Moving from an O(N2) to an O(N) problem
Challenge
- Given N domain-specific technologies
- Providing a Bridge/Gateway for each possible combination of domain-specific technologies will result in: N*(N-1)/2 = O(N^2) Bridges/Gatewas
Goal
- Overcome O(N^2) bridges/gateways problem
- Achieve Interoperability for all domain-specific technologies within Industrial Networks
- Provide the fundamental step to an Industrial Internet of Things
Solution
- Bridges/Gateways between domain-specific technology and a common Connectivity Core standard
- From O(N^2) to O(N) Bridges/Gateways
IIC concept of connectivity core gateways

- Visualization by the IIC
- Mapping domain specific connectivity technologies using gateways (remember: wireless IIoT gateways)
- Few (core) gateways between core standards
Industrial ethernet
Specification of physical connectors and MAC protocols
Wireless technologies compared

- Differentiation of technologies based on their range
- Important metrics
- Bandwidth
- Range - Licensed vs. unlicensed band
Fieldbus → Industrial Ethernet

- Same physical connectors
- Similar MAC protocols
- Depending on the real-time requirements, modification of the data link layer
IEEE TSN
- A set of layer-2 related standards for deterministic services through IEEE 802 networks
- Application domains: industrial and automotive and other deterministic networks
- Initially designed for the Audio Video Bridging (AVB) context
- Using the same connectivity technology for the office and shop floor
- Interoperable across vendors
- Core principle: Scheduling, global time, reservation
- Examples
- Frame replication and elimination for reliability: using multiple physical cables to have a backup if one cable breaks
- Frame preemption: Preemptive task scheduling known from modern operating systems
- Scheduled traffic (animation): Animation of globally synchronized scheduled slots for sending and forwarding packets
Reservation
- TSN require dynamic configuration based on application requirements
- Basically two different models for network configuration
- Distributed: Using the Stream Reservation Protocol (SRP), a bridged network can be configured in a distributed, plug-and-play manner
- Centralized: To compute network paths and transmission schedules, a CNC needs to understand the network’s physical topology. The Link Layer Discovery Protocol (LLDP) is the most common protocol.
Examples:
SRP - Talker advertisement

Step 1: Talker Advertisement
Talker = Acts as stream source and advertises the stream
Listener = Acts as stream destination and “books” the advertised stream
Domain = A set of talkers, listeners, and bridges that support the resource requirements
Reservation = A (reserved) path that provides the requested resource requirements
Stream Reservation class: A traffic class whose bandwidth can be reserved for traffic time-sensitive Streams using the Stream Reservation Protocol (SRP). A priority value is associated with each SR class. SR classes are denoted by consecutive letters of the alphabet, starting with A and continuing for up to seven classes.
SRP – Listener ready

Step 2: Propagation back to talker
Fully centralized configuration model

Centralized Network Configuration (CNC): A centralized component that configures
network resources on behalf of TSN applications (users).
Centralized User Configuration (CUC): A centralized component that discovers and
configures application (user) resources in end stations. A CUC exchanges information
with a CNC in order to configure TSN features on behalf of its end stations.
Workflow
- Talkers and Listeners communicate their stream quality of service requirements to a Centralized User Configuration (CUC) entity using an endstation specific configuration protocol.
- The CUC communicates stream quality of service requirements, on behalf of all Talker/Listener groups for its associated application, to a Centralized Network Configuration (CNC) entity using a User/Network
- The CNC performs necessary calculations to meet stream quality of service requirements in the bridged network, including calculating transmission schedules, determining data paths, etc.
- If the CNC can satisfy the end stations’ stream quality of service requirements, it configures the bridges, Talkers and Listeners