06 COMMUNICATION
OSI LAYER
OSI Layer 2(data link) +
- statistical time division multiplexing for a shared medium(Time-division multiplexing (TDM) is a method of transmitting and receiving independent signals over a common signal path by means of synchronized switches at each end of the transmission line so that each signal appears on the line only a fraction of time in an alternating pattern. It is used when the bit rate of the transmission medium exceeds that of the signal to be transmitted.)
- addressing mechanism required for multiple access
- MAC (Media Access Control) address in IEEE 802: 48 bit. Example: 98:02:97:a6:3f:44
- ARP (Address Resolution Protocol): translating between MAC and IP
- IP (Internet Protocol) address (v4): 32 bit. Example: 192.168.20.55
- Internet Control Message Protocol (ICMP): e.g. diagnose reachability of nodes
Example
- IPV4, MAC, ARP: MAC address is the hardware address, will be mapped to IP address with the help of the Address Resolution Protocol (ARP)
- ICMP: for organizing the messaging and routing. Most popular the ping command

OSI Layer 3 (Internet)
IPV4 limit
- There will be more and more connected devices that need an IP address
- The limit of the address range for IPv4 was already reached
- IPv6 is needed 128 bit instead of 32 bit
Example
IPv6 different address notation (hexadecimal instead of decimal)
Advantages
- Local address per interface
- Better handling of local networks, can also have public IPs
- Pre-defined address like local gateway or local DNS servers
- Better autoconfiguration

OSI Layer 4 (Transport)
- Transmission Control Protocol (TCP): Provides connection-based, reliable, ordered, and error-checked delivery of a stream for web, mail, file transfer, and other applications offering port numbers, handshaking, congestion control, retransmission, ...
- User Datagram Protocol (UDP): simple connectionless delivery of datagrams offering checksums and port numbers
OSI Layer 7 (Application)
- Protocols to provide functionalities for specific applications
- Examples include file transfer, remote login, mail exchange, name resolution, …
- The applications themselves are not part of this layer
- Example
- Hyper Text Transfer Protocol (HTTP) over TCP: typical client/server model
- Constrained Application Protocol (CoAP) over UDP: for constrained devices including notification
- Message Queue Telemetry Transport (MQTT) over TCP: most relevant publish/subscribe protocol currently in the IoT context
- MQTT for Sensor Networks (MQTT-SN) over UDP: for more constraint devices
- Advanced Message Queuing Protocol (AMQP): more complex publish/subscribe protocol

MIDDLEWARE
- A layer between application and the os
- In the context of distributed application is software that provides services beyond those provided by the os to enable the various components of distributed system to communicate and manage data
- Not clearly defined
- It simplifies complex distributed applications.
- Often enables interoperability
Internet of Things - communication using Internet technologies
Web of Things - communication using Web technologies

- There are no OSI layers above layer 7 – “layer 8” sometimes denoted as the “political” layer
- Invocation: defines how information can be retrieved or modified (see Remote Procedure Calls (RPC))
- Middleware: provides a set of communication services for distributed applications

OPC – OPEN PLATFORM COMMUNICATIONS
Architecture
- Coordinates the further development of the OPC standard in collaboration with users, manufacturers and researchers.
- Development and maintenance of specifications
- Certification and compliance tests of implementations
- Cooperation with other standards organizations
Motivation
- Before, the HMIs had to handle all the different protocols of the field devices
- The addition of an OPC server abstracts the different protocols away, HMIs need to implement OPC UA only
OPC COM VS. OPC UA
- OPC COM was dependent on windows OS on the devices
- OPC UA supporting a broader variety of different devices
- OPC Unified Architecture is a set of specifications applicable to manufacturing software in application areas such as Field Devices, Control Systems, Manufacturing
- Execution Systems and Enterprise Resource Planning Systems.
- These systems are intended to exchange information and to use command and control for industrial processes.
- OPC Unified Architecture defines a common infrastructure model to facilitate this information exchange.
OPC UA LAYER MODEL

OPC Unified Architecture specifies the following:
- The information model to represent structure, behavior, “semantics”, and infrastructure of the underlying real-time system.
- The message model to interact between applications.
- The communication models to transfer data between end-points.
- The conformance model to guarantee interoperability between systems.
- The security model to guarantee cyber security addressing client/server authorization, data consistency, encryption.
Operation mode 1: OPC Client-server concept

OPC implements a typical client – server architecture, where the client is responsible for management of relations with the server e.g.:
- Server discovery and localization.
- Establishing the connection.
- Generation of requests for selected data and provision of services to the server.
- Disconnection.
To establish connection with the selected server, the client must know how to address it, namely the client must know two important details:
- The network address of the workstation (usually IP address) hosting the server.
- A unique identifier of the server on the host.
Operation mode 1: OPC pubsub concept

OPC UA Spec Part 14 specifies PubSub a loosely coupled message protocol that can be used with multiple encodings (e.g. JSON, UA Binary or XML) and multiple transports (e.g. AMQP, MQTT, XMPP et. al.).